## Slide 1: The Least Secure Lock on Earth?

## Slide 2: Introduction
Seth Kintigh
  Hardware hacker
  Dell Hardware Security Engineer

## Slide 3: The TouchLock
Aluratek Touchlock
  a.k.a “Bio-Key TouchLock XL All Weather Keyless Bio-Lock with Fingerprint Recognition”
  Knockoff of TappLock?
Related locks:
  Hunting down info on FCC website I discovered there aren't just 2 of these products, but at least 8, maybe more.
  Other brands may use this same chip and code, based on product descriptions

## Slide 4: TappLock
The previous worst biometric lock was the TappLock fingerprint lock
  It effectively broadcasted its key over Bluetooth (now fixed)
  TouchLock has a Windows app instead of a phone app.
The TappLock has a “Morse Code” feature for unlocking it with a sequence of up to 12 short or long presses
  TouchLock copies that, but worse.

## Slide 5: Fingerprints as Passwords/Keys
Fingerprints are unchangeable and you leave a copy of them on literally everything you touch
  Exactly the qualities you want in a password.
  Why not protect your physical possessions with them, too?
The lock has a fingerprint reader, this is the primary intended way to unlock it
  Works well, kinda nifty

## Slide 6: Manual Brute Force Attack
2nd intended way to open it: "Morse Code“ pattern of short or long presses
  TappLock has a similar feature of 6 to 12 long patterns; keyspace is 8128 codes.
Touchlock allows exactly 6 presses for a keyspace of 2^6 or 64 possible keys.
Takes about 18 seconds to test 4 average patterns,
  All 64 will take just over 14 min, on average 7 min to crack the lock

## Slide 7: USB Brute Force attack
The lock has yet another way to open it: a PIN sent over USB from a Windows app.
  Lock identifies as a Mentor Graphics CDROM
  Windows tries to mount that drive and fails instantly, probably because it's a lock.
This PIN feature is mandatory
  If you don't set the PIN, it is still active with a default PIN
  Default PIN is set to 0000

## Slide 8: Physical Penetration
I tried prying it open and using a chisel, but the lock kept moving
  In order to keep is still I clamped in a vice, and heard some popping noises
  I tightened the clamp, heard more popping noises.
  Tightened it more, and *pop* the front popped off, revealing all the electronic and mechanics.
Not welded together
Not even screwed together
Held on by tension and a rubber gasket.
This is a very fast attack, but requires a 50 lbs vice. Not super practical.

## Slide 9: Analyzing USB Traffic
Used Wireshark for USB capture while using the PIN entry app, saw 3 packets per PIN test

## Slide 10: Analyzing USB Traffic
I analyzed the USB traffic, observed a pattern of 3 packets:
  Command Block Wrapper (CBW)
  Data transfer
  Command Status Wrapper (CSW)
Packets are Mass Storage Device USB Bulk Data transfers/SCSI

## Slide 11: The USB Attack
Python script using PyUSB library to test all possible PINs
Can test a PIN in 2 or 3 packets

## Slide 12: Company Response

## Slide 13: Conclusion
Don't buy this lock
Script available at github.com/skintigh